## Slide 1: Master’s Thesis Defense Design Space Exploration for SODA (Software-Defined Accelerator)
By: Darshith Manjunath
Committee: Dr. Chaitali Chakrabarti
Dr. Jeff Zhang
Dr. Vidya A. Chhabria

## Slide 2: Problem Definition
Design Space Exploration for SODA framework that utilizes MLIR and High-Level Synthesis (HLS) methodologies.
Growing computational demands in Deep Learning.
To optimize hardware design for best PPA using compiler optimizations.
Need for rapid hardware prototyping.

## Slide 3: Prior Work
Framework | Focus | Key Features | Limitations
POLSCA | Polybench kernels with loop transformations in HLS. | Enhances C++ code with loop transformations. | Limited to Polybench kernels, lacks neural network performance analysis.
ScaleHLS | Multi-level optimizations (graph, loop, directive) with focus on FPGAs. | Fine control over optimizations, impractical for ASICs. | Needs to be annotated back to HLS C, lacks layer-by-layer neural network analysis.
POM | FPGA-based accelerators using MLIR optimizations. | Advanced MLIR dependency analysis, layer-by-layer deep learning analysis. | Resource utilization increases with model size, problematic for ASICs.
SODA | Automated end-to-end hardware generation for both FPGA and ASIC. | Supports FPGA and ASIC, minimal manual intervention. | Loop optimization issues and ability to synthesize large neural networks.

## Slide 4: Introduction

## Slide 5: Python to GDS Pipeline
tf-mlir-translate +
tf-opt / torch-mlir
mlir-opt (protobuf to tosa and tosa to linalg)
soda-opt
mlir-opt (.mlir in llvm dialect to .ll llvm file)
Python
Bambu
OpenRoad
Verilog
GDS II Files
LLVM file

## Slide 6: SODA-OPT Flow
-soda-extract-arguments-to-xml
-soda-generate-bambu-accelcode
-soda-linalg-tile (optional)
-soda-opt-pipeline-for-bambu
-soda-outline-bambu-code

## Slide 7: MLIR Dialects in SODA-OPT
Affine dialect
Structured Control Flow (SCF) dialect
Control Flow (CF) dialect
LLVM dialect
Linalg dialect

## Slide 8: SODA-OPT Pipeline for Bambu
Linalg to Affine Loop Pass
Expanded Strided Metadata
Affine Loop Permutation
Affine Data Copy Generate
Promote Buffers to Stack
Affine Loop Unroll
Affine Loop Tiling
Lower Affine
Convert SCF to CF
Affine Scalar Replacement
Optimizations performed by SODA at affine dialect
Gold color highlight indicates loop optimization
Maroon color highlight indicates non-loop optimization

## Slide 9: Optimizations
Optimization category | Optimization | Remarks
Loop | Loop permutation | Swapping the order of nested loops.
 | Loop tiling | Breaking down a large loop into smaller blocks or tiles.
 | Loop unrolling | Expanding the loop body by replicating the operations.
Memory | Affine data copy generate | Creating local memory buffers, usually to optimize for locality.
 | Promote buffers to stack | Moves heap-allocated memory into stack-allocated memory.
 | Affine scalar replacement | Reducing memory traffic by promoting scalar values to registers.

## Slide 10: Research Goals
1. Perform Design Space Exploration (DSE) for SODA framework with loop optimizations.
2. Results analysis and heuristic development for SODA framework.
Addressing loop optimization challenges for SODA.
Fold layers to synthesize large neural networks architectures.
Derive strategies to find best optimizations for neural network architectures.
Implement these heuristics on test architectures.
Evaluate the Power, Performance, and Area (PPA) of the test architectures.
Refine SODA pipeline for Bambu.

## Slide 11: Design Space Exploration

## Slide 12: DSE Framework flow for SODA
Input file
1. Argument parsing
2. Read MLIR file
3. Create temporary MLIR files
4. Design Space Exploration (DSE)
Output file
}
File pre-processing

## Slide 13: Exploration
Types of neural network layers
Convolution layer
Depth-wise Convolution layer
Fully Connected layer
Optimizations
Loop permutation
Loop tiling
Loop unrolling
Architectures
Training architectures
Testing architectures
HLS configurations

## Slide 14: Neural Network Layer Type - 1
2D Convolution Layer
Input feature map ‘nhwc’:
n: Batch number
h: Input height
w: Input width
c: Number of input channels
Kernel ‘hwcf’:
h: Kernel height
w: Kernel width
c: Number of input channels
f: Number of output channels
Output feature map ‘nhwf’:
n: Batch number
h: Output height
w: Output width
f: Number of output channels
2D convolution layer in linalg dialect is represented by ‘linalg.conv_2d_nhwc_hwcf’.

## Slide 15: Neural Network Layer Type - 2
2D Depth-wise Convolution Layer
Depth-wise 2D convolution layer in linalg dialect is represented by ‘linalg.depthwise_conv_2d_nhwc_hwc’.
Input feature map ‘nhwc’:
n: Batch number
h: Input height
w: Input width
c: Number of input channels
Kernel ‘hwcm’:
h: Kernel height
w: Kernel width
c: Number of input channels
Output feature map ‘nhwcm’:
n: Batch number
h: Output height
w: Output width
c: Number of input channels

## Slide 16: Neural Network Layer Type - 3
Fully Connected Layer
Fully Connecter layer in linalg dialect is represented by ‘linalg.batch_matmul’.
Input feature map ‘nhw’:
n: Batch number
h: Input height
w: Input width
Weight matrix:
n: Batch number
h: Weight matrix height
w: Weight matrix width
Output feature map ‘nhw’:
n: Batch number
h: Output height
w: Output width

## Slide 17: Optimization
Loop permutation
Output-first permutation for Convolution layer
Kernel-first permutation for Convolution layer
Convolution layer has 72 permutations to explore. 36 each for Output-first and Kernel-first permutations.
Depth-wise Convolution 24 permutations to explore. 12 each for Output-first and Kernel-first permutations.
FC layer has 6 different permutations to explore.

## Slide 18: Optimization
Loop tiling
For FC layer, output height, output width, and kernel width are tiled in powers of 2 from 4 to the maximum dimension.
For Conv. and D-Conv. layers output height/width, kernel height/width and input channels are tiled.
FC layer before tiling
FC layer tiled to size 16

## Slide 19: Optimization
Loop unrolling
For FC layer with no. of unrolls 1 and 2 with factors 4, 8, 16, and full-unroll are performed.
For Conv. and D-Conv. layers with no. of unrolls 1, 2, and 3 with factors 4, 8, 16, until full-unroll are performed.
FC layer before unrolling
Unroll 1 with Full-unroll
Unroll 1 with factor 16

## Slide 20: Architectures Explored
No. | Model | No. of Conv. Layers | No. of D-Conv. Layers | No. of FC Layers | Total No. of Layers Explored
1 | LeNet | 3 | NA | 2 | 5
2 | AlexNet | 5 | NA | 3 | 8
3 | VGG-16 | 13 | NA | 3 | 16
4 | MobileNetV3-Small | - | 11 | NA | 11
Total |  | 21 | 11 | 8 | 40
No. | Model | No. of Conv. Layers | No. of D-Conv. Layers | No. of FC Layers | Total No. of Layers Explored
1 | VGG-19 | 16 | NA | 3 | 19
2 | ResNet-18 | 20 | NA | 1 | 21
3 | MobileNetV3-Large | - | 15 | NA | 15
Total |  | 36 | 15 | 4 | 55
Observed heuristics from:
Tested heuristics on:

## Slide 21: HLS Configurations
Configuration | Values | Remarks
Maximum clock cycles | (2^32)-1 | Accommodates maximum allowable no. of clock cycles by Bambu’s testbench.
Frequency | 100MHz | No timing violations are observed at this frequency.
Memory allocation policy | NO_BRAM | Memory modules should not be synthesized. Memory modules are usually places as macros in ASICs.
PDK | NanGate45 | NanGate45 is a commonly used open-source PDK for 45nm technology.

## Slide 22: Refinements for Exploration
Refinements for SODA pipeline
Affine Scalar Replacement
Affine data copy generate
Loop optimization order
Loop optimization issues
Loop permutation – 1 issue
Loop tiling – 2 issues
Loop unrolling – 2 issues
Folding neural network layers
Depth-wise Convolution mapping

## Slide 23: Refined SODA-OPT Pipeline for Bambu
Linalg to Affine Loop Pass
Expanded Strided Metadata
Affine Loop Tiling
Affine Scalar Replacement
Affine Loop Unroll
Affine Data Copy Generate
Affine Loop Permutation
Lower Affine
Convert SCF to CF
Promote Buffers to Stack
New order of optimizations performed by SODA at affine dialect
Gold color highlight indicates loop optimization
Maroon color highlight indicates non-loop optimization

## Slide 24: Refined SODA-OPT Pipeline for Bambu
Affine Scalar replacement
Problem: Repeated access of scalar values with loops.
Effect: The number of scalar variables increases after unrolling, resulting in inefficiencies in the loop's performance. It is possible that SODA struggles at this stage while attempting to replace all the scalars
Impact: Reduces redundant memory accesses, simplifies unrolled loops, and improves overall loop performance.
Solution: Apply affine scalar replacement before loop unrolling to move scalar variables to registers.
Affine Loop Tiling
Affine Scalar Replacement
Affine Loop Unroll
Affine Data Copy Generate
Affine Loop Permutation
Promote Buffers to Stack

## Slide 25: Refined SODA-OPT Pipeline for Bambu
Affine data copy generate
Problem: Unrolling buffer storage loop.
Effect: Buffer storage loops are created before unrolling, leading to unnecessary bottlenecks in the operation. Additionally, this process can significantly increase the time required to generate MLIR files.
Impact: Streamlined memory operations, reduced buffer overhead, and more efficient handling of expanded loop structures.
Solution: Apply affine data copy generation after loop unrolling to avoid unrolling buffers storing loop.
Affine Loop Tiling
Affine Scalar Replacement
Affine Loop Unroll
Affine Data Copy Generate
Affine Loop Permutation
Promote Buffers to Stack

## Slide 26: Refined SODA-OPT Pipeline for Bambu
Loop optimization order
Affine Loop Tiling
Affine Scalar Replacement
Affine Loop Unroll
Affine Data Copy Generate
Affine Loop Permutation
Promote Buffers to Stack
Problem: Performing loop permutation after loop tiling.
Challenge: Loop permutation following loop tiling creates an overly expansive exploration space, hindering optimization efficiency.
Solution: Reorder the optimizations to apply loop permutation before loop tiling, ensuring a more structured and manageable loop nest for permutation.
Impact: Every optimization builds on top of previous optimization’s improvements.

## Slide 27: Loop Optimization Issues
Loop permutation
Problem 2: Permutation mapping doesn’t work correctly. The issue is in MLIR-OPT.
Problem 1: Cannot give permutation order to SODA.
Create custom set of passes to use perform loop permutation.
Created CSV files for all 3 linalgs to map correctly.
Permutation No. | Permutation tried | Does it work?
1 | 0,1,2,3 | Yes
2 | 0,1,3,2 | Yes
3 | 0,2,1,3 | Yes
4 | 0,2,3,1 | No (This maps to - 0,3,1,2)
5 | 0,3,1,2 | No (This maps to - 0,2,3,1)
6 | 0,3,2,1 | Yes
Layer Type | No. of permutations that map correctly | Total No. of permutations | % of correctly mapped permutations
linalg.conv2d_nhwc_hwcf | 22 | 72 | 30.56%
linalg.depthwise_conv_2d_nhwc_hwc | 10 | 24 | 41.67%
linalg.batch_matmul | 4 | 6 | 66.67%
Total | 36 | 102 | 35.30%

## Slide 28: Loop Optimization Issues
Loop tiling
Issue 1: Uniform Tile Size Limitation in SODA Pipeline for Bambu
Problem: The SODA pipeline for Bambu only allows one uniform tile size, which limits flexibility in applying tiling optimizations.
Solution: Use the "Affine Tile Sizes" pass and create a custom set of passes to explore different tile sizes and optimize the process.
Issue 2: Promote Buffers to Stack Pass
Problem: The "Promote Buffers to Stack" pass causes the affine loop tiling pass to fail, throwing an error.
Solution: Remove the "Promote Buffers to Stack" pass entirely to allow the affine loop tiling pass to execute without errors, enabling successful tiling optimizations.

## Slide 29: Loop Optimization Issues
Loop unrolling
Issue 1: Affine Scalar Replacement
Problem: Performing Affine Scalar Replacement too early can cause significant delays in replacing all scalars in the unrolled affine loop.
Solution: Perform loop unrolling after scalar replacement to efficiently handle scalars in unrolled loops.
Issue 2: Buffer Trick
Problem: Using temporary buffers to store intermediate values combined with loop unrolling creates an excess of buffers, complicating the synthesis process (e.g., using tools like Bambu for Verilog generation).
Solution: Remove the buffer trick for unrolling to simplify the number of buffers and streamline the synthesis process.

## Slide 30: Folding layers
Test bench has a time limit on how many cycles the design under test can be run for.
Input channels are folded according to input feature map dimension.
All the output channels are folded to 1.
Convolution and Depth-wise Convolution layers:
Fully Connected Layers: All the dimensions are folded to 128 for permutation and tiling) and folded to 32 for unrolling.
Further folding is done for unrolling.
Estimate total clock cycles for a layer by multiplying the clock cycles per tile by the number of tiles in the layer.
I/p feature map height/width | Max I/p channels
<=16 | 128
>16 and <=32 | 32
> 32 and <=64 | 8
> 64 | 1
CNN layers folding for loop unrolling |  | 
I/p height/width | Kernel height/width | Max I/p channels
<=64 | <=3 | 32
 | >3 and <=5 | 8
 | > 5 and <=7 | 4
 | > 7 | 1
>64 | 1 - 11 | 1

## Slide 31: Depth-wise Convolution Mapping
The depth-wise convolution with multiplier doesn’t perform well with certain loop optimizations, so we map it to the depth-wise convolution with no multiplier.
It helps with mapping any type of depth-wise convolution to the same kind of layer to explore.
linalg.depth_conv2d_nhwc_hwc at affine level:
linalg.depth_conv2d_nhwc_hwcm at affine level:
Configuration | Clock cycles
Baseline | 673,486
Unroll - 3 | 673,486
Configuration | Clock cycles
Baseline | 673,486
Unroll - 3 | 198,092

## Slide 32: Results

## Slide 33: Results Evaluated
Parameters | Remarks | Formula
Clock cycles | Number of clock cycles required to complete a layer of the neural network. | N
Runtime | Duration needed to process a single layer of the neural network, measured in seconds. | T = N / frequency
Total Power | Power consumption of the ASIC during operation, measured in watts. | P
Area | Physical area occupied by the ASIC layout, measured in square micro meters (µm²). | -
GFLOPS | Indicates the computational performance of the ASIC, measured in Giga FLOPS. | GFLOPS = FLOP count / T
GFLOPS/W | Represents the energy efficiency of the ASIC, calculated as performance per watt. | GFLOPS/W = GFLOPS / P
Energy | Energy consumed by the ASIC in Joules. | E = P * T
Main goal is to evaluate Power, Performance and Area (PPA) along with efficiency.

## Slide 34: Permutation - CNN Layer
Case: Kernels with no. of input channels > 1 - Results
AlexNet CNN Layer 3:
Layer info | Input |  |  | Kernel |  |  |  | Output |  | 
 | H | W | C | H | W | C | F | H | W | F
Actual | 15 | 15 | 256 | 3 | 3 | 256 | 384 | 13 | 13 | 256
Executed | 15 | 15 | 32 | 3 | 3 | 32 | 1 | 13 | 13 | 1
Permutation | Clock cycles | Total power | Area | Runtime | GFLOPS | GFLOPS/W | Energy
0,1,2,3,4,5,6 | 841,064,448 | 0.0123 | 109,121 | 8.410644 | 0.035555 | 2.89065 | 0.103451
Permutation | Clock cycles | Total power | Area | Runtime | GFLOPS | GFLOPS/W | Energy
0,1,2,3,5,6,4 | 691,414,272 | 0.0115 | 103,378 | 6.914143 | 0.043251 | 3.760957 | 0.079513
Best Output-first permutation:
Permutation | Clock cycles | Total power | Area | Runtime | GFLOPS | GFLOPS/W | Energy
0,4,5,6,1,2,3 | 981,087,744 | 0.0135 | 118,153 | 9.810877 | 0.030481 | 2.257852 | 0.132447
Best Kernel-first permutation:
Baseline permutation:
Output-first permutation always yields the best performance.

## Slide 35: Permutation – CNN Layer
Case: Kernels with no. of input channels > 1 - Methodology
Permutation | Clock cycles | Total power | Area | Runtime | GFLOPS | GFLOPS/W | Energy
0,1,2,3,4,5,6 | 841,064,448 | 0.0123 | 109121 | 8.410644 | 0.035555 | 2.89065 | 0.103451
0,1,2,3,4,6,5 | 691,414,272 | 0.0114 | 103105 | 6.914143 | 0.043251 | 3.793947 | 0.078821
0,1,2,3,5,4,6 | 841,064,448 | 0.0122 | 108384 | 8.410644 | 0.035555 | 2.914344 | 0.10261
0,1,2,3,5,6,4 | 691,414,272 | 0.0115 | 103378 | 6.914143 | 0.043251 | 3.760957 | 0.079513
0,1,2,3,6,4,5 | 691,414,272 | 0.0107 | 98348 | 6.914143 | 0.043251 | 4.04215 | 0.073981
0,1,2,3,6,5,4 | 691,414,272 | 0.0117 | 99618 | 6.914143 | 0.043251 | 3.696667 | 0.080895
Sweep (kernel permutation): Sweep the kernel dimensions and get the best permutation.
Only kernel dimensions input provides performance improvement.

## Slide 36: Permutation – D-CNN
Case: Kernels with no. of input channels > 1 - Results
Mobilenet-v3-small D-CNN Layer 2:
Layer info | Input |  |  | Kernel |  |  | Output |  | 
 | H | W | C | H | W | C | H | W | C
Actual | 57 | 57 | 72 | 3 | 3 | 72 | 28 | 28 | 72
Executed | 57 | 57 | 8 | 3 | 3 | 8 | 28 | 28 | 8
Permutation | Clock cycles | Total power | Area | Runtime | GFLOPS | GFLOPS/W | Energy
0,1,2,3,4,5 | 2,948,913 | 0.0118 | 96,654 | 0.029489 | 0.034456 | 2.92 | 0.000348
Permutation | Clock cycles | Total power | Area | Runtime | GFLOPS | GFLOPS/W | Energy
0,3,2,1,5,4 | 2,379,933 | 0.0123 | 101,655 | 0.023799 | 0.042694 | 3.471057 | 0.000293
Best permutations (Output first permutation):
Permutation | Clock cycles | Total power | Area | Runtime | GFLOPS | GFLOPS/W | Energy
0,5,3,4,2,1 | 3,808,440 | 0.0112 | 94,712 | 0.038084 | 0.02668 | 2.382143 | 0.000427
Best permutations (Kernel first permutation):
Baseline permutation:
Output-first permutation always yields the best performance.

## Slide 37: Permutation – FC Layer
Case 1: Small layers - Results
Permutation | Clock cycles | Total power | Area | Runtime | GFLOPS | GFLOPS/W | Energy
0,1,2,3 | 7,652 | 0.00601 | 52,803.0 | 7.7e-05 | 0.021818 | 3.630283 | 4.6277e-07
0,1,3,2 | 4,706 | 0.00659 | 61,364.0 | 4.7e-05 | 0.035745 | 5.424127 | 3.0973e-07
0,2,1,3 | 7,652 | 0.00595 | 52,454.0 | 7.7e-05 | 0.021818 | 3.666891 | 4.5815e-07
0,2,3,1 | 7,652 | 0.00595 | 52,441.0 | 7.7e-05 | 0.021818 | 3.666891 | 4.5815e-07
0,3,1,2 | 4,706 | 0.00661 | 61,975.0 | 4.7e-05 | 0.035745 | 5.407716 | 3.1067e-07
0,3,2,1 | 4,706 | 0.00659 | 61,931.0 | 4.7e-05 | 0.035745 | 5.424127 | 3.0973e-07
For smaller FC layers, loop permutations (0,1,3,2) or (0,3,1,2) or (0,3,2,1) could be picked to get best performance, power efficiency at the cost of area.
Layer info | Input |  | Weights |  | Output | 
 | H | W | H | W | H | W
Actual | 1 | 84 | 84 | 10 | 1 | 10
Executed | 1 | 84 | 84 | 10 | 1 | 10
LeNet Fully Connected (FC) Layer 2:
Dataset with small number of classes like MNIST need to use this loop permutation to get best performance.

## Slide 38: Permutation – FC Layer
Case 2: Large layers - Results
Permutation | Clock cycles | Total power | Area | Runtime | GFLOPS | GFLOPS/W | Energy
0,1,2,3 | 317,721,600.0 | 0.00415 | 32,699.0 | 3.177216 | 0.023762 | 5.725783 | 0.0131854464
0,1,3,2 | 355,175,424.0 | 0.00398 | 32,030.0 | 3.551754 | 0.021256 | 5.340704 | 0.01413598092
0,2,1,3 | 317,721,600.0 | 0.00408 | 32,329.0 | 3.177216 | 0.023762 | 5.82402 | 0.01296304128
0,2,3,1 | 317,721,600.0 | 0.00415 | 32,699.0 | 3.177216 | 0.023762 | 5.725783 | 0.0131854464
0,3,1,2 | 355,175,424.0 | 0.00398 | 32,030.0 | 3.551754 | 0.021256 | 5.340704 | 0.01413598092
0,3,2,1 | 355,175,424.0 | 0.00398 | 32,030.0 | 3.551754 | 0.021256 | 5.340704 | 0.01413598092
For smaller FC layers, loop permutations (0,1,3,2) or (0,3,1,2) or (0,3,2,1) could be picked to get best performance, power efficiency at the cost of area.
Layer info | Input |  | Weights |  | Output | 
 | H | W | H | W | H | W
Actual | 1 | 9216 | 9216 | 4096 | 1 | 4096
Executed | 1 | 128 | 128 | 128 | 1 | 128
AlexNet Fully Connected (FC) Layer 1:
Dataset with large number of classes like ImageNet need to use this loop permutation to get best performance.

## Slide 39: Tiling - CNN
Case 1: Kernels with no. of input channels > 1 - Results.
AlexNet CNN Layer 5:
Layer info | Input |  |  | Kernel |  |  |  | Output |  | 
 | H | W | C | H | W | C | F | H | W | F
Actual | 15 | 15 | 384 | 3 | 3 | 384 | 256 | 13 | 13 | 256
Executed | 15 | 15 | 128 | 3 | 3 | 128 | 1 | 13 | 13 | 1
Tile | Clock cycles | Total power | Area | Runtime | GFLOPS | GFLOPS/W | Energy
None | 841,099,008 | 0.0137 | 111,099 | 8.41099 | 0.035554 | 2.595182 | 0.115231
Tile | Clock cycles | Total power | Area | Runtime | GFLOPS | GFLOPS/W | Energy
1,13,13,1,3,3,16 | 695,159,040 | 0.0196 | 170,582 | 6.95159 | 0.043018 | 2.194796 | 0.136251
Best configuration:
Baseline configuration:
Best tiling configuration depends on the layer’s input dimensions.

## Slide 40: Tiling - CNN
Case 1: Kernels with no. of input channels > 1 - Methodology
Chart: Clock cycles
| 4 | 8 | 16 | 32 | 64 | 128
O/p tile size - 4 | 710890752 | 700912896 | 695923968 | 843631104 | 842228736 | 841238784
O/p tile size - 8 | 708913920 | 699919104 | 695421696 | 843214848 | 841830912 | 841135872
O/p size - 13 | 707877120 | 699398400 | 695159040 | 843081216 | 841761792 | 841099008
Chart: GFLOPS
| 4 | 8 | 16 | 32 | 64 | 128
O/p tile size - 4 | 0.042066 | 0.042664 | 0.04297 | 0.035447 | 0.035506 | 0.035548
O/p tile size - 8 | 0.042183 | 0.042725 | 0.043001 | 0.035464 | 0.035523 | 0.035552
O/p size - 13 | 0.042245 | 0.042757 | 0.043018 | 0.03547 | 0.035526 | 0.035554
Chart: Area
| 4 | 8 | 16 | 32 | 64 | 128
O/p tile size - 4 | 113190 | 132824 | 175114 | 120422 | 119980 | 115482
O/p tile size - 8 | 108208 | 129053 | 169841 | 116162 | 115722 | 112491
O/p size - 13 | 108120 | 128272 | 170582 | 116297 | 115782 | 111099
Chart: Power
| 4 | 8 | 16 | 32 | 64 | 128
O/p tile size - 4 | 0.0127 | 0.0152 | 0.0208 | 0.014 | 0.0137 | 0.0135
O/p tile size - 8 | 0.012 | 0.0162 | 0.0214 | 0.0135 | 0.013 | 0.0124
O/p size - 13 | 0.013 | 0.0146 | 0.0196 | 0.0137 | 0.0137 | 0.0137
Input channel tiled to 16 yield best performance.

## Slide 41: Tiling - CNN
Case 2: Kernel tiling
Tile | Clock cycles | Total power | Area | Runtime | GFLOPS | GFLOPS/W | Energy
1,8,8,1,3,3,4 | 2,059,048,704 | 0.0156 | 142,327 | 20.59049 | 0.043505 | 2.788782 | 0.321212
1,8,8,1,3,3,8 | 1,975,428,864 | 0.015 | 132,551 | 19.75429 | 0.045347 | 3.023133 | 0.296314
1,8,8,1,3,3,16 | 1,933,594,368 | 0.0162 | 144,709 | 19.33594 | 0.046328 | 2.859753 | 0.313242
1,8,8,1,3,3,32 | 2,360,451,840 | 0.0153 | 134,921 | 23.60452 | 0.03795 | 2.480392 | 0.361149
Kernel tiled to size 3:
Tile | Clock cycles | Total power | Area | Runtime | GFLOPS | GFLOPS/W | Energy
1,8,8,1,5,5,4 | 1,911,125,760 | 0.0169 | 154,230 | 19.11126 | 0.046873 | 2.77355 | 0.32298
1,8,8,1,5,5,8 | 1,912,603,392 | 0.0145 | 129,005 | 19.12603 | 0.046836 | 3.230069 | 0.277327
1,8,8,1,5,5,16 | 1,902,144,768 | 0.0156 | 137,951 | 19.02145 | 0.047094 | 3.018846 | 0.296735
1,8,8,1,5,5,32 | 2,347,600,128 | 0.0144 | 127,741 | 23.476 | 0.038158 | 2.649861 | 0.338054
No kernel tiling:
Kernel tiling gives bad performance. Always exclude kernel tiling in exploration.
Layer info | Input |  |  | Kernel |  |  |  | Output |  | 
 | H | W | C | H | W | C | F | H | W | F
Actual | 31 | 31 | 96 | 5 | 5 | 96 | 256 | 27 | 27 | 256
Executed | 31 | 31 | 32 | 5 | 5 | 32 | 1 | 27 | 27 | 1
AlexNet CNN Layer 2:

## Slide 42: Tiling – FC layer
Results
AlexNet Fully Connected (FC) Layer 3:
Layer info | Input |  | Weights |  | Output | 
 | H | W | H | W | H | W
Actual | 1 | 4096 | 4096 | 1000 | 1 | 1000
Executed | 1 | 128 | 128 | 125 | 1 | 125
Tile | Clock cycles | Total power | Area | Runtime | GFLOPS | GFLOPS/W | Energy
None | 34,511,104 | 0.00454 | 36,055 | 0.345111 | 0.023737 | 5.228414 | 0.001567
Tile | Clock cycles | Total power | Area | Runtime | GFLOPS | GFLOPS/W | Energy
1,1,64,16 | 31,124,736 | 0.0142 | 118,464.0 | 0.311247 | 0.02632 | 1.853521 | 0.0044197074
Baseline configuration:
Best configuration:
Best tiling configuration depends on whether the layer is a hidden layer or output layer.

## Slide 43: Tiling – FC layer
Methodology
First sweep (Tiling innermost loop): The configuration 1,1,4,16 provides the best performance. Fix innermost loop tile to 16.
Second sweep (Tiling outer loop): The optimal tiling configuration for the fully connected layer is 1,1,64,16.
Tile | Clock cycles | Total power | Area | Runtime | GFLOPS | GFLOPS/W | Energy
1,1,4,4 | 35,244,032 | 0.0059 | 51,098 | 0.35244 | 0.023244 | 3.939661 | 0.002079396
1,1,4,8 | 33,314,816 | 0.00748 | 62,642 | 0.333148 | 0.02459 | 3.287433 | 0.002491947
1,1,4,16 | 32,350,208 | 0.00978 | 83,972 | 0.323502 | 0.025323 | 2.589264 | 0.00316385
1,1,4,32 | 39,007,488 | 0.00634 | 55,984 | 0.390075 | 0.021001 | 3.312461 | 0.002473076
1,1,4,64 | 34,655,488 | 0.00484 | 43,138 | 0.346555 | 0.023638 | 4.883884 | 0.001677326
1,1,4,128 | 34,527,488 | 0.00471 | 37,766 | 0.345275 | 0.023726 | 5.037367 | 0.001626245
Tile | Clock cycles | Total power | Area | Runtime | GFLOPS | GFLOPS/W | Energy
1,1,4,16 | 32,350,208 | 0.00978 | 83,972 | 0.323502 | 0.025323 | 2.589264 | 0.00316384956
1,1,8,16 | 31,719,424 | 0.00979 | 84,101 | 0.317194 | 0.025826 | 2.637998 | 0.00310532926
1,1,16,16 | 31,404,032 | 0.00992 | 84,888 | 0.31404 | 0.026086 | 2.629637 | 0.0031152768
1,1,32,16 | 31,246,336 | 0.00983 | 84,589 | 0.312463 | 0.026218 | 2.667141 | 0.00307151129
1,1,64,16 | 31,124,736 | 0.0142 | 118,464 | 0.311247 | 0.02632 | 1.853521 | 0.0044197074
1,1,125,16 | 31,125,504 | 0.00956 | 80,886 | 0.311255 | 0.026319 | 2.753033 | 0.0029755978

## Slide 44: Unrolling - CNN
Case 1: Unrolling larger kernel width/height with no. of input channels 1 - Results
AlexNet CNN Layer 1:
Layer info | Input |  |  | Kernel |  |  |  | Output |  | 
 | H | W | C | H | W | C | F | H | W | F
Actual | 227 | 227 | 3 | 11 | 11 | 3 | 96 | 55 | 55 | 96
Executed | 227 | 227 | 1 | 11 | 11 | 1 | 1 | 55 | 55 | 1
No. of unrolls | Unroll Factor | Clock cycles | Total power | Area | Runtime | GFLOPS | GFLOPS/W | Energy
0 | 0 | 425,162,016 | 0.00398 | 39,522 | 4.25162 | 0.049588 | 12.459296 | 0.0169214476
1 | Full-unroll | 425,162,016 | 0.004 | 39,614 | 4.25162 | 0.049588 | 12.397 | 0.01700648
2 | 4 | 425,162,016 | 0.004 | 39,607 | 4.25162 | 0.049588 | 12.397 | 0.01700648
2 | 8 | 425,162,016 | 0.004 | 39,542 | 4.25162 | 0.049588 | 12.397 | 0.01700648
2 | Full-unroll | 425,162,016 | 0.00395 | 39,395 | 4.25162 | 0.049588 | 12.553924 | 0.016793899
3 | 4 | 396,422,208 | 0.0168 | 152,200 | 3.964222 | 0.053183 | 3.165655 | 0.0665989296
3 | 8 | 318,195,072 | 0.0312 | 251,698 | 3.181951 | 0.066258 | 2.123654 | 0.0992768712
3 | Full-unroll | 318,350,592 | 0.0322 | 248,566 | 3.183506 | 0.066226 | 2.056708 | 0.1025088932
With larger kernel size and no. of input channels being 1, the effects of unrolling is seen after unrolling inner-most loops 3 times.

## Slide 45: Unrolling - CNN
Case 2: Unrolling kernels with no. of input channels > 1 - Results
AlexNet CNN Layer 5:
Layer info | Input |  |  | Kernel |  |  |  | Output |  | 
 | H | W | C | H | W | C | F | H | W | F
Actual | 15 | 15 | 384 | 3 | 3 | 384 | 256 | 13 | 13 | 256
Executed | 15 | 15 | 32 | 3 | 3 | 32 | 1 | 13 | 13 | 1
No. of unrolls | Unroll Factor | Clock cycles | Total power | Area | Runtime | GFLOPS | GFLOPS/W | Energy
0 | 0 | 750,243,840 | 0.00497 | 45,452 | 7.502438 | 0.039859 | 8.01992 | 0.03728711686
1 | 4 | 603,319,296 | 0.00436 | 39,082 | 6.033193 | 0.049566 | 11.368349 | 0.02630472148
1 | 8 | 606,434,304 | 0.00327 | 29,279 | 6.064343 | 0.049311 | 15.079817 | 0.01983040161
1 | 16 | 606,434,304 | 0.00491 | 39,412 | 6.064343 | 0.049311 | 10.042974 | 0.02977592413
1 | Full-unroll | 601,761,792 | 0.00755 | 65,218 | 6.017618 | 0.049694 | 6.581987 | 0.0454330159
2 | Full-unroll | 600,204,288 | 0.0232 | 177,517 | 6.002043 | 0.049823 | 2.147543 | 0.1392473976
3 | Full-unroll | 457,986,048 | 0.0649 | 509,320 | 4.57986 | 0.065295 | 1.006086 | 0.297232914
As we unroll further loops fully, performance improves further at a significant penalty of power, area, and efficiency.
Unrolling 1 with unrolling factor 4, 8, 16 yields performance while also improving on power, area, and efficiency.

## Slide 46: Unrolling – D-CNN
Case: Unrolling kernels with no. of input channels > 1 - Results
Mobilenet-v3-small
D-CNN Layer 2:
Unrolls | Unroll Factor | Clock cycles | Total power | Area | Runtime | GFLOPS | GFLOPS/W | Energy
0 | 0 | 2,203,914 | 0.00377 | 36,695 | 0.022039 | 0.046103 | 12.22891 | 8.31E-05
1 | Full-unroll | 2,203,914 | 0.00375 | 36,261 | 0.022039 | 0.046103 | 12.29413 | 8.26E-05
2 | Full-unroll | 2,203,914 | 0.00374 | 35,808 | 0.022039 | 0.046103 | 12.32701 | 8.24E-05
3 | 4 | 1,357,194 | 0.00941 | 88,117 | 0.013572 | 0.074865 | 7.955898 | 0.000128
3 | 8 | 1,230,186 | 0.0166 | 152,923 | 0.012302 | 0.082593 | 4.975482 | 0.000204
3 | 16 | 1,173,036 | 0.042 | 343,284 | 0.01173 | 0.086621 | 2.062405 | 0.000493
3 | Full-unroll | 645,180 | 0.0579 | 466,803 | 0.006452 | 0.15748 | 2.719862 | 0.000374
Unroll-3 improves performance. Unroll factor improves performance without smaller power and area penalties compared to full-unroll.
Layer info | Input |  |  | Kernel |  |  | Output |  | 
 | H | W | C | H | W | C | H | W | C
Actual | 57 | 57 | 72 | 3 | 3 | 72 | 28 | 28 | 72
Executed | 57 | 57 | 24 | 3 | 3 | 24 | 28 | 28 | 24

## Slide 47: Unroll - FC Layer
AlexNet Fully Connected (FC) Layer 1:
Layer info | Input |  | Weights |  | Output | 
 | H | W | H | W | H | W
Actual | 1 | 9216 | 9216 | 4096 | 1 | 4096
Executed | 1 | 32 | 32 | 32 | 1 | 32
No. of Unrolls | Unroll Factor | Clock cycles | Total power | Area | Runtime | GFLOPS | GFLOPS/W | Energy
0 | 0 | 155,787,264 | 0.0014 | 12,258 | 1.557873 | 0.048462 | 34.615714 | 0.0021810222
1 | 4 | 118,038,528 | 0.0088 | 70,710 | 1.180385 | 0.06396 | 7.218962 | 0.0104582111
1 | 8 | 118,038,528 | 0.0088 | 70,417 | 1.180385 | 0.06396 | 7.202703 | 0.0104818188
1 | 16 | 118,038,528 | 0.0088 | 71,035 | 1.180385 | 0.06396 | 7.194601 | 0.01049362265
1 | full-unroll | 118,038,528 | 0.0088 | 70,921 | 1.180385 | 0.06396 | 7.251701 | 0.0104109957
2 | 4 | 59,645,952 | 0.0228 | 178,788 | 0.59646 | 0.126576 | 5.551579 | 0.013599288
2 | 8 | 50,208,768 | 0.0383 | 323,216 | 0.502088 | 0.150367 | 3.926031 | 0.0192299704
2 | 16 | 45,490,176 | 0.0711 | 575,059 | 0.454902 | 0.165964 | 2.334233 | 0.0323435322
2 | full-unroll | 43,057,152 | 0.166 | 1,146,979 | 0.430572 | 0.175342 | 1.056277 | 0.071474952
Unrolling 1 with any factor doesn’t make any difference to the performance.
Unrolling 2 with factors does improve performance at the cost of power, area and efficiency.

## Slide 48: Heuristics
Convolution layer
I/p feature map height/width | Loop permutation | Loop tiling | Loop unrolling
size <=16 | 0,1,2,3,5,6,4 | 1,<actual o/p height>,<actual o/p width>,1, <actual kernel height>,<actual kernel width>,16 | Unroll 3 - Full unroll
16 < size <=32 | 0,1,2,3,5,6,4 | 1,8,8,1,<actual kernel height>,<actual kernel width>,16 | Unroll 3 - Full unroll
32 < size <=64 | 0,1,2,3,5,6,4 | Baseline | Unroll 3 - Full unroll
size > 64 | Baseline | Baseline | Baseline
For input feature map sizes greater than 64, where both input and output channels are equal to one, no loop optimization techniques are effective. In this scenario, the baseline configuration provides the best performance.

## Slide 49: Heuristics
Depth-wise Convolution layer
I/p feature map height/width | Loop permutation | Loop unrolling
size <=16 | 0,3,2,1,5,4 | Unroll 3 - Full unroll
16 < size <=32 | 0,3,2,1,5,4 | Unroll 3 - Full unroll
32 < size <=64 | 0,3,2,1,5,4 | Unroll 3 - Full unroll
size > 64 | Baseline | Baseline
For input feature map sizes greater than 64, where both input and output channels are equal to one, no loop optimization techniques are effective. In this scenario, the baseline configuration provides the best performance.

## Slide 50: Heuristics
Fully Connected layer
Type | Loop permutation | Loop tiling | Loop unrolling
Hidden layer | Baseline | 1,1,4,4 | Unroll 2 - Full unroll
Output layer | Baseline | 1,1,64,16 | Unroll 2 - Full unroll
Output layer is assumed to be for ImageNet dataset with 1000 classes.

## Slide 51: Predicting on Test Architectures
VGG-19 |  |  | 
Layer No. | Layer type | Best permutation configuration | Heuristic
1 - 4 | Conv2D | Baseline | ✓
5 - 16 | Conv2D | 0,1,2,3,5,6,4 | ✓
17 - 19 | FC | Baseline | ✓
ResNet-18 |  |  | 
Layer No. | Layer type | Best permutation configuration | Heuristic
1 | Conv2D | Baseline | ✓
2 - 7 | Conv2D | 0,1,2,3,5,6,4 | ✓
8 | Conv2D | Baseline | ✘
9 - 12 | Conv2D | 0,1,2,3,5,6,4 | ✓
13 | Conv2D | Baseline | ✘
14 - 17 | Conv2D | 0,1,2,3,5,6,4 | ✓
18 | Conv2D | Baseline | ✘
19-20 | Conv2D | 0,1,2,3,5,6,4 | ✓
21 | FC | Baseline | ✓
Loop permutation
MobileNetV3-Large |  |  | 
Layer No. | Layer type | Best permutation configuration | Heuristic
1-2 | D-Conv2D | Baseline | ✓
3-15 | D-Conv2D | 0,3,2,1,5,4 | ✓
Certain configurations within the Convolutional layers are not achieving optimal permutation configurations using the current heuristics.
In contrast, the heuristics are effectively determining the best permutation configurations for the Depth-wise Convolutional layers and Fully Connected layers.

## Slide 52
Chart: Runtime of VGG-19 layers
Baseline | 2.7943 | 59.6107 | 42.3248 | 84.6496 | 40.8966 | 81.7931 | 81.7931 | 81.7931 | 51.337 | 102.674 | 102.674 | 102.674 | 25.9442 | 25.9442 | 25.9442 | 25.9442 | 8.6491 | 1.4121 | 0.34488
Best | 2.7943 | 59.6107 | 42.3248 | 84.6496 | 31.5226 | 63.0452 | 63.0452 | 63.0452 | 42.0565 | 84.1129 | 84.1129 | 84.1129 | 21.316 | 21.316 | 21.316 | 21.316 | 8.6491 | 1.4121 | 0.34488
Chart: Power of VGG-19 layers
Baseline | 0.00386 | 0.00361 | 0.0073 | 0.0073 | 0.0112 | 0.0109 | 0.011 | 0.011 | 0.017 | 0.0171 | 0.016 | 0.0168 | 0.0127 | 0.013 | 0.0126 | 0.0123 | 0.0041 | 0.00415 | 0.00417
Best | 0.00386 | 0.00361 | 0.00719 | 0.00718 | 0.0215 | 0.022 | 0.0219 | 0.0211 | 0.0153 | 0.0151 | 0.0152 | 0.0152 | 0.0115 | 0.0121 | 0.0114 | 0.0115 | 0.0041 | 0.00415 | 0.00417
Chart: Area of VGG-19 layers
Baseline | 34519 | 34236 | 59012 | 59012 | 98159 | 96967 | 97129 | 96602 | 137496 | 136313 | 138061 | 137657 | 107670 | 108145 | 107584 | 108334 | 32388 | 32699 | 34714
Best | 34519 | 34236 | 60140 | 60125 | 169786 | 169084 | 169701 | 169807 | 133223 | 132966 | 132412 | 132556 | 103181 | 103568 | 103102 | 103398 | 32388 | 32699 | 34714
Conv. 32 < I/p size <= 64
Conv. I/p size <= 32
Conv. I/p size > 64
FC layer
Loop permutation for convolution improves performance. But the variation in power and area depends on the size of the i/p layer size.
FC layer doesn’t see any difference as baseline is the best configuration.

## Slide 53
Chart: Runtime of MNV3-Large D-Conv. layers
Baseline | 0.082666 | 0.1072 | 0.10313 | 0.065994 | 0.10961 | 0.10961 | 0.03039 | 0.020564 | 0.01892 | 0.01892 | 0.049383 | 0.069087 | 0.045093 | 0.057841 | 0.057841
Best | 0.082666 | 0.1072 | 0.080307 | 0.051284 | 0.08518 | 0.08518 | 0.025729 | 0.01669 | 0.015356 | 0.015356 | 0.04015 | 0.056072 | 0.036749 | 0.045932 | 0.045932
Chart: Power of MNV3-Large D-Conv. layers
Baseline | 0.00706 | 0.00755 | 0.0119 | 0.0174 | 0.0128 | 0.0128 | 0.0117 | 0.00943 | 0.00936 | 0.00939 | 0.00942 | 0.00913 | 0.0156 | 0.0189 | 0.0189
Best | 0.00706 | 0.00755 | 0.0122 | 0.0183 | 0.0129 | 0.013 | 0.0124 | 0.00975 | 0.00978 | 0.00979 | 0.00966 | 0.00928 | 0.016 | 0.0193 | 0.0193
Chart: Area of MNV3-Large D-Conv. Layers
Baseline | 58371 | 62845 | 97490 | 144201 | 110683 | 110366 | 98881 | 79278 | 79305 | 79688 | 81708 | 77401 | 131190 | 169522 | 169627
Best | 58371 | 62845 | 101117 | 150538 | 113047 | 113726 | 103182 | 83032 | 82699 | 82976 | 85012 | 80307 | 135384 | 172953 | 171698
I/p size > 64
I/p size <= 64
Loop permutation helps improve performance with marginal penalties in power and area.

## Slide 54: Predicting on Test Architectures
VGG-19 |  |  | 
Layer No. | Layer Type | Best Tiling configuration | Heuristic
1-8 | Conv2D | Baseline | ✓
9-12 | Conv2D | 1,8,8,1,3,3,16 | ✓
13-16 | Conv2D | 1,14,14,1,3,3,16 | ✓
17-18 | FC | 1,1,4,4 | ✓
19 | FC | 1,1,64,16 | ✓
ResNet-18 |  |  | 
Layer No. | Layer Type | Best Tiling configuration | Heuristic
1-7 | Conv2D | Baseline | ✓
8 | Conv2D | 1,4,4,1,1,1,4 | ✘
9-10 | Conv2D | 1,8,8,1,3,3,16 | ✓
11 | Conv2D | 1,14,14,1,3,3,8 | ✘
12 | Conv2D | 1,14,14,1,3,3,16 | ✓
13 | Conv2D | 1,14,14,1,1,1,16 | ✓
14-15 | Conv2D | 1,14,14,1,3,3,16 | ✓
16-17 | Conv2D | 1,7,7,1,3,3,16 | ✓
18 | Conv2D | 1,7,7,1,1,1,16 | ✓
19-20 | Conv2D | 1,7,7,1,3,3,16 | ✓
21 | FC | 1,1,64,16 | ✓
Loop tiling
Heuristics work for FC layer. But, for Convolution layers the heuristic fails to find the best tiling configuration on 2 occasions.

## Slide 55
Chart: Runtime of VGG-19 layers
Baseline | 2.7943 | 59.6107 | 42.3248 | 84.6496 | 40.9077 | 81.8154 | 81.8154 | 81.8154 | 51.3408 | 102.6816 | 102.6816 | 102.6816 | 25.9452 | 25.9452 | 25.9452 | 25.9452 | 8.6547 | 1.413 | 0.34511
Best | 2.7943 | 59.6107 | 42.3248 | 84.6496 | 40.9077 | 81.8154 | 81.8154 | 81.8154 | 42.402 | 84.804 | 84.804 | 84.804 | 21.4395 | 21.4395 | 21.4395 | 21.4395 | 6.3327 | 1.0339 | 0.31125
Chart: Power of VGG-19 layers
Baseline | 0.00386 | 0.00361 | 0.0073 | 0.0073 | 0.0129 | 0.0133 | 0.0129 | 0.0128 | 0.0201 | 0.0199 | 0.0217 | 0.0201 | 0.0132 | 0.0136 | 0.0132 | 0.0133 | 0.00439 | 0.00439 | 0.00454
Best | 0.00386 | 0.00361 | 0.0073 | 0.0073 | 0.0129 | 0.0133 | 0.0129 | 0.0128 | 0.0203 | 0.0202 | 0.0204 | 0.0204 | 0.0179 | 0.0184 | 0.0184 | 0.0183 | 0.00771 | 0.00784 | 0.0144
Chart: Area of VGG-19 layers
Baseline | 34519 | 34236 | 59012 | 59012 | 114047 | 114073 | 114033 | 113666 | 173617 | 172815 | 173472 | 173954 | 116487 | 116376 | 116741 | 117287 | 34421 | 34421 | 36055
Best | 34519 | 34236 | 59012 | 59012 | 114047 | 114073 | 114033 | 113666 | 175638 | 175037 | 175884 | 175927 | 159632 | 160834 | 160761 | 161826 | 68090 | 68280 | 117726
Conv. I/p size > 32
Conv. 16 < I/p size <= 32
Conv. I/p size <= 16
FC hidden layer
FC o/p layer
Improvement in PPA depends on size of Conv. layer size.
FC hidden layer improves performance with penalties in power and area.
Output layer marginally improves performance, with significant penalties in power and area.

## Slide 56: Predicting on Test Architectures
Unrolling – VGG19 |  |  | 
Layer No. | Layer Type | Unrolling configuration | Heuristics
1-4 | Conv2D | Baseline | ✓
5-16 | Conv2D | Unroll 3 - Full-unroll | ✓
17-19 | FC | Unroll 2 - Full-unroll | ✓
Loop unrolling
MobileNetV3-Large |  |  | 
Layer No. | Layer Type | Unrolling configuration | Heuristics
1-2 | D-Conv2D | Baseline | ✓
3-15 | D-Conv2D | Unroll 3 - Full-unroll | ✓
ResNet-18 |  |  | 
Layer No. | Layer Type | Unrolling configuration | Heuristics
1 | Conv2D | Baseline | ✓
2-20 | Conv2D | Unroll 3 - Full-unroll | ✓
21 | FC | Unroll 2 - Full-unroll | ✓
Loop unrolling heuristics works correctly for all the layers tried.

## Slide 57
Chart: Runtime of VGG-19 layers
Baseline | 2.7943 | 59.6107 | 29.8107 | 59.6214 | 46.4034 | 92.8067 | 92.8067 | 92.8067 | 46.404 | 92.808 | 92.808 | 92.808 | 23.2027 | 23.2027 | 23.2027 | 23.2027 | 4.2409 | 0.69239 | 0.16906
Best | 2.7943 | 59.6107 | 29.8107 | 59.6214 | 27.9517 | 55.9034 | 55.9034 | 55.9034 | 28.0638 | 56.1277 | 56.1277 | 56.1277 | 14.1473 | 14.1473 | 14.1473 | 14.1473 | 1.1721 | 0.19137 | 0.047872
Chart: Power of VGG-19 layers
Baseline | 0.00386 | 0.00361 | 0.00371 | 0.0037 | 0.00499 | 0.00499 | 0.005 | 0.00499 | 0.00487 | 0.00489 | 0.00489 | 0.0049 | 0.00487 | 0.00487 | 0.00488 | 0.0052 | 0.0014 | 0.0014 | 0.00164
Best | 0.00386 | 0.00361 | 0.00371 | 0.0037 | 0.0629 | 0.0616 | 0.0624 | 0.0627 | 0.063 | 0.0616 | 0.0627 | 0.0626 | 0.0636 | 0.0618 | 0.0637 | 0.0648 | 0.165 | 0.164 | 0.132
Chart: Area of VGG-19 layers
Baseline | 34519 | 34236 | 34078 | 34075 | 45778 | 45800 | 45844 | 45808 | 44630 | 44708 | 44707 | 44743 | 44032 | 44036 | 44088 | 43820 | 12258 | 12258 | 13532
Best | 34519 | 34236 | 34078 | 34075 | 504355 | 508176 | 507439 | 507618 | 506111 | 505051 | 506726 | 505361 | 505974 | 498824 | 499898 | 504406 | 1145763 | 1147639 | 912028
Conv. I/p size > 64
Conv. I/p size > 64
FC layer
Loop permutations provide substantial performance improvements; however, they also incur a significant penalty in power consumption and area, particularly for fully connected (FC) layers.

## Slide 58
Chart: Runtime of MNV3-Large D-Conv. Layers
Baseline | 0.058224 | 0.058248 | 0.088155 | 0.058215 | 0.097146 | 0.097146 | 0.018363 | 0.015305 | 0.014082 | 0.014082 | 0.036755 | 0.051456 | 0.034012 | 0.048521 | 0.048521
Best | 0.058224 | 0.058248 | 0.025601 | 0.018753 | 0.031255 | 0.031255 | 0.005421 | 0.004554 | 0.004205 | 0.004205 | 0.010822 | 0.015151 | 0.011471 | 0.016387 | 0.016387
Chart: Power of MNV3-Large D-Conv. Layers
Baseline | 0.00397 | 0.00373 | 0.00372 | 0.0074 | 0.00772 | 0.00741 | 0.004 | 0.00397 | 0.0041 | 0.00409 | 0.0036 | 0.00361 | 0.00757 | 0.00768 | 0.00742
Best | 0.00397 | 0.00373 | 0.057 | 0.0476 | 0.0475 | 0.0475 | 0.0728 | 0.0657 | 0.0591 | 0.0597 | 0.0748 | 0.0735 | 0.0477 | 0.0487 | 0.0475
Chart: Area of MNV3-Large D-Conv. Layers
Baseline | 35181 | 34753 | 36433 | 71165 | 68459 | 68849 | 37999 | 37638 | 37528 | 37571 | 32719 | 32734 | 69676 | 73090 | 71994
Best | 35181 | 34753 | 462793 | 386160 | 378087 | 375383 | 599745 | 541228 | 493141 | 499164 | 596315 | 594037 | 383447 | 390335 | 390406
I/p size > 64
I/p size <= 64
Loop permutations provide substantial performance improvements; however, they also incur a significant penalty in power consumption and area.

## Slide 59: Summary
Layer Type | Optimization | Power | Performance | Area | Efficiency | Energy
Convolution Layer | Loop Permutation | * | ⬆ | * | * | *
 | Loop Tiling | ⬆ | ⬆ | ⬆ | ⬇ | ⬆
 | Loop Unrolling | ⬆ | ⬆ | ⬆ | ⬇ | ⬆
Depth-wise Convolution Layer | Loop Permutation | ⬆ | ⬆ | ⬆ | ⬆ | ⬇
 | Loop Tiling | ✘ |  |  |  | 
 | Loop Unrolling | ⬆ | ⬆ | ⬆ | ⬇ | ⬆
Fully Connected Layer | Loop Permutation | - |  |  |  | 
 | Loop Tiling | ⬆ | ⬆ | ⬆ | ⬇ | ⬆
 | Loop Unrolling | ⬆ | ⬆ | ⬆ | ⬇ | ⬆
Symbol | Remarks
⬆ | Increase in value
⬇ | Decrease in value
- | No change in value
✘ | Doesn’t work
* | Varies based on the specific case, such as layer size (large or small).
Highlight label
Indicates good change
Indicates bad change

## Slide 60: Conclusion

## Slide 61: Thesis contribution
1. Performed Design Space Exploration (DSE) with loop optimizations.
2. Analysed results and developed heuristics for SODA framework.
Addressed loop optimization challenges for SODA framework.
Explored folding layers to synthesize large neural networks.
Derived heuristics from training architectures.
Implemented these heuristics on alternative architectures.
Evaluated the Power, Performance, and Area (PPA) of the test architectures.
Refined SODA pipeline for Bambu.

## Slide 62: Future work
1. Explore loop pipelining.
2. Explore for combinations of loop optimizations (For e.g., loop permutation + loop tiling).
3. Apply linalg tiling + affine tiling to larger CNN layers to see improvement in performance with tiling.
5. Examine the effects of quantization of CNN layers on performance using ‘linalg.conv_2d_nhwc_hwcf_q’.
4. Explore loop optimizations for pooling, activation layers, and skip connection layers.

## Slide 63
THANK YOU!

## Slide 64: DSE Command Line Arguments
Type | Parameters | Remarks
MLIR | --read_mlir | Read Neural Network MLIR file (E.g. Resnet-18).
Loop optimization | --permute | Performs loop permutation.
 | --tile | Performs loop tiling.
 | --unroll | Performs loop unrolling.
Type of NN layer | --conv2d | Explores 2D Convolution layers.
 | --depthwise_conv2d | Explores 2D Depth-wise Convolution layers.
 | --matmul | Explores 2D Fully Connected layers.
Layer options | --start_layer | (Optional) Select layer no. to start exploring from.
 | --end_layer | (Optional) Select layer no. to end exploring at.
 | --select_layer | (Optional) Select a particular layer to explore.

## Slide 65: What if you actually need to simulate the entire number of channels?

## Slide 66: SODA Linalg Tile

## Slide 67: SODA Linalg Tile

## Slide 68: SODA Linalg Tile
-soda-linalg-tile pass creates ASIC with the given tile sizes.
The main requirement for tiling dimensions is that the tiling dimension has to be a factor of the actual dimension.
Example: Let’s say a certain CNN layer has 88 output channels. Now this output channel can be tiled to one of its factors, e.g. 44. But it can’t be tiled to 32, as it is not a factor of 88.
For this, test-bench will have to be modified to remove the simulation time limit. If Verilator doesn’t finish simulation within its time limit.

## Slide 69: Affine Loop Permutation - 2D Convolution
Output first permutation
Kernel first permutation